## Slide 1: Demo application – UHF temperature sensing tags
ASYGN AS3213T tags
Hendrik Schnabel

## Slide 2: Introduction
This document will provide the basic fundamentals of the UHF RFID sensor transponder and mainly cover the following topics:
    Types of available IC / Solutions
    Introduction of demo tools
      ARGEE V3 demo
      CODESYS V3.5 SP16
  It will also contain ideas on potential applications, but no success stories or real world examples.
  If i can be of assistance or you want to provide feedback to this document or technology, please do not hesitate to contact me.
Hendrik Schnabel
Product Manager UHF RFID systems
+49 151 16773699
Hendrik.Schnabel@turck.com

## Slide 3: AS3213T – Temperature
Key facts
Below some key facts about the temperature sensing element.
The sensor itself is capable to operate even in higher temperature environments than standard IC. Most standard IC on the market are only capable of maximum +80/+85°C operation temperature.
* A typical read operation of the tag itself lasts ~10ms, so compared to a standard read operation of an EPC, the duration of the measurement does not affect the total duration of a reading cycle!
** Accuracy can be recalibrated, but the operating temperature range than changes from
Parameter | Min | Typ | Max | Unit
Operating temperature range | -40 |  | +125 | °C
Storage temperatue range | -70 |  | +250 | °C
Resolution |  | ± 0.35 |  | 
Measurement time |  | 140* |  | µs
Typ. accuracy (after calibration) |  | ± 2** |  | °C
The sensor IC is made by the company asygn, which is based in France (Grenoble). Their key focus is electronic system design for RF but also general sensor interfaces as well as RFID sensing IC.
You will find more information about the company on their website: www.asygn.com and the product itself in the attached PPT about the use cases.
Samples for initial tests can be provided via the product management – even if hard tags through our main tag supplier are available, the label tags (from identytag) are easier to get.

## Slide 4: Example – Temperature sensing with ASYGN AS3213T IC
UHF reader demo setup (example)
Features and requirements
FEATURES
Easy demo for usage of temperature sensor tags
Read and calculate Integrated temperature sensor with RFID-U-interface
Integrated HMI for easy demo purposes (ARGEE)
Calculation formulas implemented in ARGEE and CODSYS V3
REQUIREMENTS
ARGEE
„ASYGN_AS3213T_demo_V3.arg“
ARGEE V3 programing environment
ARGEE V3 compatible device with RFID-U-interface (TBEN-S2-2RFID-4DXP, TBEN-Lx-4RFID-8DXP, TN-UHF-Q150-…-EN or similar)
CODESYS
„Temperatue_calculation_ASYGN_AS3213T.projectarchive “
CODESYS V3.5 SP16 or later
RFID-U-interface compatible devices (TBEx-S2-2RFID-4DXP, TBEx-Lx-4RFID-8DXP, TN-UHF-Q150-…, TN-UHF-Qxxx-…-CDS or similar)

## Slide 5: ARGEE V3
NOTE: Load the ARGEE project into your device and press „RUN“
„Run“ the program
Press „Read Tag“
Result displayed in „temperature“

## Slide 6: CODESYS V3.5 SP16
NOTE: Please check all IP adresses and Profinet names ahead
„Run“ the program
Write „TRUE“ into variable „xSTART“
Result displayed
1.
2.
3.